## Slide 1: High-Performance Cordless AB Series
10000 SE Pine St., Portland, OR 97216 • (503) 254-6600 • (800) 852-1368 • www.aimco-global.com
Recover Your Tool
using AcraDyne Tool Manager Software

## Slide 2: Recovery
In order to start tool recovery, connect the tool your PC using the USB cable.

## Slide 3: Recovery
Make sure you have the latest version of AcraDyne Tool Manager software. The software is available on the AIMCO website.
Any new release is backward-compatible. Please delete old versions of the software.
Log on as Administrator.
Admin

## Slide 4: Recovery
Click on the USB icon.

## Slide 5: Recovery
When the tool connects successfully, you will see “connected” on the lower left of the screen.

## Slide 6: Recovery
Click on the folder icon, which is the “load saved configuration” button.

## Slide 7: Recovery
Browse either for the latest tool backup file or the initial tool settings.
Click “Open.”

## Slide 8: Recovery
If using a tool backup file, Tool Manager will ask if you would like to recover the tool.
Acknowledge with OK.

## Slide 9: Recovery
If you are not using a backup of the tool itself, Tool Manager will ask which parts of the tool you
would like to recover.
Acknowledge with OK.

## Slide 10: Recovery
Click on “write” to save the data to the tool.
The tool should be ready to use.

## Slide 11: Thank You
10000 SE Pine St., Portland, OR 97216 • (503) 254-6600 • (800) 852-1368 • www.aimco-global.com
www.aimco-global.com